General comments, can be of any length.
Please note that the program uses equal, number and : signs as special recognizers!
The results are written to the sub-directory output'

Simulation parameters
Relaxed wake (yes 1, no 0): relax =	0	choice of wake model
Steady (1) or unsteady (2): aerodynamics =	1	=2 Quasi unsteady I (no apparent mass)
Viscous solutions (1) or inviscid (0) viscous =	0	=1 to estimate profile drag, airfoil files have to exist
Using camber (1) or no camber (0) camber	=	1	=1 than camber files have to exist (Fig. 1)
Symmetrical geometry (yes 1, no 0): sym =	0	=1 only right wing is modeled
Pitch trim (yes 1, no 0):	trimPITCH =	0	trim flags
Roll trim (yes 1, no 0):	trimROLL =	0
Lift trim (yes 1, no 0):	trimCL =	1	=1 will iterate to match target CL,
CL = 2W cos(phi)/{density Uinf^2 S}

Max. number of time steps:	maxtime =	20	number of timesteps
Width of each time step (sec):	deltime =	.5	Defines timestep size (with Uinf)
Convergence delta-span efficiency: deltae =	0.00	(0 if only timestepping) convergence criteria
freestream flow condition
Freestream velocity (leave value 1):	Uinf =	10
AOA beginning, end, step size [deg]:	alpha=	5 15 1	if trimCL != 1 than alpha sweep
Sideslip angle [deg]:	beta =	0	5 to 15 deg every 1deg
Turning flight conditions
Circling flight information
Circling flight on (1) off (0):	circling = 0
Turning in horizontal plane (1)	horizontal = 0 if (0), a/c descends
Bank angle (deg)	phi = 20	bank angle
Upwind velocity (m/s)	Ws = 0	if there is a vertical velocity
Velocity gradient (1/s)	gradient = .3864	velocity gradient when turning.
If set to circling !=0 => gradient = (9.81 * tan(info.bank)) / (info.Uinf)

Density:	density =	1.225
Kinematic viscosity:	nu =	1.420000e-05

Reference area:	S =	20
Reference span:	b =	20

Mean aerodynamic chord:	cmac =	1
Aircraft weight (N):	W =	3000.0
CG location (x y z):	cg = 0.25 0 0	cg location (x,y,z)
CMo of wing:	CMo =	0.000	additional CM, obsolete

No. of wings (max. 5):	wings =	2	a t-tail is a single wing
No. of panels:	panels =	5	several panels define a wing
No. of airfoils (max. 15):	airfoils	= 2	defines how many camber and/or airfoil files need to be provided
general review of some parameters
Panel boundary conditions:
Symmetry line -	10
Between panels -	220
Free end -	100

Hinge is in percentage chord:
Midchord -	0.5
Leading edge -	0
NO HINGE -	1

Defines leading edge of wing, all measured in metres:
Definition of panels that describe the geometry. Each panel has nxm DVEs in the spanswise and chordwise direction, respectively. Each panel can have unique n and m values.
Left wing panel
Panel #:1. Number of elements across span n = 5 and chord m = 6
Neighbouring panels (0 for none) left: 0 right: 2	panel at the right and left of panel. If 0 than no neighbouring panel
left edge information: x,y,z, chord length, incidence angle, bound. Cond., airfoil (camber, airfoil), hinge location/deflection
xleft	yleft	zleft	chord	epsilon	Bound.Cond. Airfoil Hinge Deflection
0.0	-10	0.00	1.00	0.00	100	6	0.75	0
xright	yright	zright	chord	epsilon	Bound.Cond. Airfoil Hinge Deflection
0.0	0	0.000 1. 0.000	220	6	0.75	0
right wing panel
Panel #:2. Number of elements across span n = 5 and chord m = 6
Neighbouring panels (0 for none) left: 1 right: 3
xleft	yleft	zleft	chord	epsilon	Bound.Cond. Airfoil Hinge Deflection
0.0	0	0.00	1.00	0.00	220	6	0.75	0
xright	yright	zright	chord	epsilon	Bound.Cond. Airfoil Hinge Deflection
0.0	10	0.000	1.	0.000	100	6	0.75	0
left horizontal tail panel
Panel #:3. Number of elements across span n = 3 and chord m = 4
Neighbouring panels (0 for none) left: 0 right: 4
xleft	yleft	zleft	chord	epsilon	Bound.Cond. Airfoil Hinge Deflection
10.15	-2.00	2.00	0.600	.00	100	6	0.75	0
xleft	yleft	zleft	chord	epsilon	Bound.Cond. Airfoil Hinge Deflection
10.15	.00	2.00	0.600	.00	220	6	0.75	0
right horizontal tail panel
Panel #:4. Number of elements across span n = 3 and chord m = 4
Neighbouring panels (0 for none) left: 3 right: 0
xleft	yleft	zleft	chord	epsilon	Bound.Cond. Airfoil Hinge Deflection
10.15	.00	2.00	0.600	.00	220	6	0.75	0
xleft	yleft	zleft	chord	epsilon	Bound.Cond. Airfoil Hinge Deflection
10.15	2.00	2.00	0.600	.00	100	6	0.75	0
vertical tail panel
Panel #:5. Number of elements across span n = 2 and chord m = 4
Neighbouring panels (0 for none) left: 0 right: 4
xleft	yleft	zleft	chord	epsilon	Bound.Cond. Airfoil Hinge Deflection
10.15	.00	.00	0.600	.00	100	6	0.75	0
xleft	yleft	zleft	chord	epsilon	Bound.Cond. Airfoil Hinge Deflection
10.15	.00	2.00	0.600	.00	220	6	0.75	0

old definitions related to fuselage and empennage drag, obsolete but can be reactivated.
%<- special identifier
Vertical tail information:
Number of panels (max 5) = 0
no.	chord	area	airfoil

Fuselage information:
Number of sections (max 20) =	0
Width of each section =	0.000
Panel where transition occurs =	0
No.	Diamter

Interference drag = 0.0%
##############